## Slide 1: Pump by Priority
Priority Scoring Overview

## Slide 2: Pump by Priority Scoring
PRIORITY SCORE
PRIORITY FOR VISIT
LOSING REVENUE
HIGH #
LOW #
Layer 1
Layer 2
🚚 Oil or Water Run Ready
🚚 Oil or Water Run Ready this Weekend
⚠️ Tank Over 90% Full
👷 Gauge Ready
📅 Gauge Ready on Weekend
👓 Recent Workover, Visual Inspection Needed
⚙️ Repeat Failure Well
👷👓 Risk Based Visit Required
🕒 Split Connect
🕒 Plunger Change Required
CRITICAL
HIGH
MEDIUM
LOW
ROUTINE
📉 Below Forecast Aries Forecast
🛠️ Downtime (Lost Production)
🚨 MCFD SCADA Variance to Yesterday

## Slide 3: Priority Rank Example
Revenue Variance
Oil (& Water Ready)
Water Ready
Recent Workovers
Repeated Failures
Gauge Ready
Injection Well
Routine visit / Scheduled visit
Outperforming wells
HIGHEST PRIORITY
LOWEST PRIORITY
PUMP BY PRIORITY RANKING
Highest to Lowest
BOPD (high to low)
BWPD (high to low)
BFPD (high to low)
Daily cash flow (high to low)
BFPD (high to low)
BWPD (high to low)
BOEPD (high to low)
Daily Revenue (high to low)
REVENUE VARIANCE RANGE | PRIORITY SCORE
>$750 | 5
$300 < CF <= $750 | 4
$200 < CF <= $300 | 3
$100 < CF <= $200 | 2
$10 < CF <= $100 | 1
CF < 10 | 0
URGENCY FOR VISIT | PRIORITY SCORE
Urgent | 5
High | 4
Medium | 3
Low | 2
Routine | 1
Layer 1
Layer 2
Score and Priority Assignment
CRITICAL
HIGH
MEDIUM
LOW
ROUTINE
MAVERICK WELL

## Slide 4: Priority Rank Example
P1
Score and Priority Assignment
Rev: $2000
P2
P3
P4
P5
Rev: $1800
Rev: $1600
Rev: $1400
Layer 3: Coordinate / Route Planning
P7
P8
P6
Oil Run Ready
PR: 200 BOPD
Oil Run Ready
PR: 115 BOPD
H2O Run Ready
PR: 11 BWPD
Gauge Ready
PR:100 BFPD
Rev = Revenue Variance
PR = Production Rate
PX = Priority #X
Revenue Variance
Oil (& Water Ready)
Water Ready
Recent Workovers
Repeated Failures
Gauge Ready
Injection Well
Routine visit / Scheduled visit
Outperforming wells
HIGHEST PRIORITY
LOWEST PRIORITY
PUMP BY PRIORITY RANKING
Highest to Lowest
BOPD (high to low)
BWPD (high to low)
BFPD (high to low)
Daily cash flow (high to low)
BFPD (high to low)
BWPD (high to low)
BOEPD (high to low)
Daily Revenue (high to low)
CRITICAL
HIGH
MEDIUM
LOW
ROUTINE

## Slide 5: Pump by Priority Flags
📉 Below Forecast
  Routine to Critical - based on Revenue/day Variance to Aries Live
      $10 - $100 (Routine) ꟷ $100 - $200 (Low) ꟷ $200 - $300 (Medium)
      $300 - $750 (High) ꟷ > $750 (Critical)
🛠️ Downtime (Lost Production)
  Routine to Critical - based on Revenue/day Variance to Aries Live
      $10 - $100 (Routine) ꟷ $100 - $200 (Low) ꟷ $200 - $300 (Medium)
      $300 - $750 (High) ꟷ > $750 (Critical)
🚨 MCFD SCADA Variance to Yesterday
  Routine to Critical - based on SCADA Gas Revenue/day Variance to Yest.
  Must be greater than $50 in revenue variance and over 50% diff in MCFD
      $10 - $100 (Routine) ꟷ $100 - $200 (Low) ꟷ $200 - $300 (Medium)
      $300 - $750 (High) ꟷ > $750 (Critical)
Cash Flow – Layer 1
Risk & Visit – Layer 2
🚚 Oil or Water Run Ready
  Medium to High
    Escalates to High when:
      Avg Runs per day over last 180 days >= 0.5
🚚 Oil or Water Run Ready this Weekend
  Medium to High
    Medium on Thursday
    High on Friday
⚠️ Tank Over 90% Full
  Medium
👷 Gauge Ready
  Low to Medium - based on days since 50% or 75% of load ready
      0 days (Low) ꟷ 1 or more days overdue (Medium)
📅 Gauge Ready on Weekend
  Low: Thursday (50% Gauge)
  Medium: Thursday (75% Gauge) or Friday (50% Gauge)
  High: Friday (75% Gauge)
👓 Recent Workover, Visual Inspection Needed
  Medium (first 3 days post workover)
⚙️ Repeat Failure Well
  Routine to Medium based on days since last visit
      0-6 days (Routine) ꟷ 7-13 days (Low) ꟷ >=14 day (Medium)
👷👓 Risk Based Visit Required
  Routine to High - based on days since last visit & Risk Matrix
🕒 Split Connect
  High – Sales line change required per schedule
🕒 Plunger Change Required
  Routine to Critical – Plunger change required per schedule, based on Layer 1 Priority Score
FYI Flags – No Scoring
📌 Primary Priority Score Flag/s
🛠️ Subsurface/Downhole Failure
🐿️ Invalid Downtime Code (From SCADA)
🧭 Tubing Pressure Variance Exceeds 75% and is >= +/- 25 psi
🧭 Casing Pressure Variance Exceeds 75% and is >= +/- 25 psi
🧭 Flowline Pressure Variance Exceeds 75%
📋 Missing Disposition
📈 Above Forecast